## Microtan Capture Listing

- List Program on Microtan using I command.  Capture on Hyperterminal.  Save as .TXT.

- Run Excel

- Open with listing captured above.  Set delimited fields using ‘Space’ (ie at 5, 12 & 16).  Set all as TEXT.

- Sheet will be labelled with capture filename. Save as List1, XLSX format.

- Open MicrotanMakeSource.xlsx spreadsheet.  Save with new filename (eg NewFile)

- Copy data generated in List1 and paste into NewFile sheet ‘Ifiledump’ starting at cell A2.  Close List1

## Create Labels

- Copy data area in columns A- D from cell A2 to the bottom-right cell in column D  in sheet ‘Ifiledump’ and paste into the next sheet ‘LabelSheet’ columns at Cell A2

- Copy E1-M1 down to the bottom of the listing

- Adjust bottom-right value of ‘TableEFG ‘ to align with the bottom cell in column A (use CNTRL F3 to edit the ‘table’ definition – the last numeric value will require amendment).  The range will be $E$2:$G$xx.

- Save Spreadsheet.

- Address any ? In column L.  If data rather than assembly code, insert DEFB in Column C and delete fields in column D.

- Search for any BIT commands.  Check if they have 3 bytes, they should be DEFB instead.

## Linking Check

- Copy column G in sheet ‘LabelSheet’  and PASTE SPECIAL (Values) into LinkCheck sheet column A.  Select Column A in ‘LinkCheck’ sheet and Sort (under Excel Data menu item) Note: do not expand selection. Select Column A in ‘LinkCheck’ sheet and Remove Duplicates (under Excel Data menu item) Note: do not expand selection.

- Copy column I in sheet ‘LabelSheet’  and PASTE SPECIAL (Values) into LinkCheck sheet column B.  Select Column B in ‘LinkCheck’ sheet and Sort (under Excel Data menu item) Note: do not expand selection. Select Column B in ‘LinkCheck’ sheet and Remove Duplicates (under Excel Data menu item) Note: do not expand selection.

- Use Control F3 to adjust the bottom value of the Labels range to fit Column B data ie $B$2:$B$xx

- Copy C1 to D1 down to align with bottom of column A.   Column C will show any anomalies where an Operand address exists that does not have a corresponding Label. Every Operand pointing to an address within the program range should have a Label.  Check every Operand address pointing outside the program range is real.  Fix the anomalies and repeat the Linking Check.

## Create Source Listing

- For Labels outside of the range of the program listing, copy LinkCheck columns C to D and PASTE SPECIAL (Values) into ‘Source’ sheet at A1.

- On ‘Source’ sheet type * into Column A of the next row below the existing data.  Type =$nnnn into Column B of the next row below the existing data, where nnnn is the start address of the code to be assembled.

- Copy LabelSheet columns K to M and PASTE SPECIAL (values) into Source sheet columns A to C below existing data.

## Create Listing

- For Labels outside of the range of the program listing, copy LinkCheck columns C to D and PASTE SPECIAL (Values) into ‘Listing’ sheet at A1.

- On ‘Listing’ sheet type * into Column E of the next row below the existing data.  Type =$nnnn into into Column F of the next row below the existing data, where nnnn is the start address of the code to be assembled.

- Copy LabelSheet columns A and B and PASTE into Listing sheet columns A and B below existing data.

- Copy LabelSheet columns K to M and PASTE SPECIAL (Values) into Listing sheet columns D to F below existing data.

## Prepare Source for Data Entry

- Copy Source sheet into WORD.

- Select (Double click table) and Convert TABLE to TEXT in “Layout” using TAB separators

- Save file as Plain Text (MSDOS) using CR only line ends

- Load MSDOS file into HxD.

- Replace Hex-values 09 with 20.

- Replace Hex-values 20 20 with 20

- Replace Hex-values 20 0D with 0D

- Replace Hex-values 0D 0D with 0D

- Replace Hex-values 0D 20 with 0D

- Save file

## Laptop Prep

- Run Hyperterminal

- Properties – ASCII settings – delay 20mS characters and 500ms line ends

- Echo typed Characters

## Microtan Prep

- Load DASM (R8000,9FFF,0,C000)

- MD7A4 = 01

- MBFD2 = 09

- Run C000 (ie type GC000)

- (Do not enter any further commands)

## Laptop

- Enter Initialisation data (Y followed by 2000<CR>)

- Send command N1 for auto line numbering

- Send ASCII text File

- Exit using M command or Reset.

## Microtan

- Restart DASM (GC000)

- N to Initialise?

- Save file. ‘D’ to tape, ‘W’ to disk